QINGDAO WEICHANG INDUSTRY AND TRADE CO., LTD

Add:Yanjialing Industrial Park,Tongji Office,Jimo,Qingdao

Sales manager: Kiki; Email:sales008@kingiso.com

Mob: 86-18563934279    Tel: 86-532-80999854

WVP2300B Vacuum membrane press

The finishing show:

Technical parameters:

| Overall dimension | 2500x2700x1150mm |
| --- | --- |
| Worktable size | 2300x1100mm |
| Total Power | 25kw |
| Vacuum pressure | -0.1Mpa |
| Weight | 500kg |
| The Max.Thickness | 2500x2700x1150mm |

Characteristic:

- Design unique,small footprint,innovative,easy to operate.Easy to isolate the individual space.

- Saving energy,this machine achieved that when we need to heating then heating ,when we do not need to heat then without heating.So it save much energy.

- This machine use near-infrared heating pipe,heating fast and temperature higher.Thereby solving the problem of long time of pre-heating,it saving 30minutes of waiting time.

- Direct connect vacuum pump,low noise,small size,high technology content.

- The high degree of automation,installation easy,simple operation,easy to learn.